## Slide 1
Future Inundation Frequency of Coastal Critical Facilities
Dr. Tom Herrington
Associate Director

## Slide 2: Introduction
Coastal Critical Facilities and Marine Dependent Industries are exposed to higher climate change risk due to their required proximity to coastal waters for:
  Maritime Transportation
  Cooling Waters
  Effluent Discharge
  Supply Chain & Transportation Networks

## Slide 3: “Infrastructure currently designed for historical climate conditions is more vulnerable to future weather extremes and climate change.”
- 4th National Climate Assessment

## Slide 4: Coastal Climate Change Risks
Sea Level Rise
  Nuisance Flooding
  Chronic Flooding
  Storm Surge
Saltwater Intrusion
Increasing Seawater Temperature
Increase in Precipitation Intensity & Frequency
Shoreline Erosion
Focus of today’s talk

## Slide 5: Flooding Terminology -What are we really talking about?
Nuisance Flooding - flooding that
causes public inconveniences such
as frequent road closures (NOAA)
Chronic Flooding - flooding that
occurs more than 26 times per year
or every 2 weeks on average
(Union of Concerned Scientists)
Storm Surge – the abnormal rise in seawater level during a storm, measured as the height of the water above the normal predicted astronomical tide

## Slide 6: The Issue: Relative Sea Level Rise

## Slide 7: Relative Sea Level Rise at Atlantic City, NJ

## Slide 8: Result: More Days Like This
Annapolis, MD

## Slide 9: Sea Level Rise Impact on Total Water Levels
Chart: Influence of Sea Level Rise on Water Elevation at Atlantic City
Minor Flood | 3.38 | 3.38
Moderate Flood | 4.38 | 4.38
Minor
Flood
Moderate
Flood

## Slide 10: Future Impact: 2074
Chart: Influence of Sea Level Rise on Water Elevation at Atlantic City
Minor Flood | 3.38 | 3.38
Moderate Flood | 4.38 | 4.38
Major Flood | 5.38 | 5.38
Minor
Flood
Moderate
Flood
Major
Flood

## Slide 11: Sea Level Rise is projected to accelerate
Estimated, Observed and Projected Sea Level Rise (Melillo et al., 2014)

## Slide 12: Concern
How frequently will low-lying roadways and infrastructure experience flooding in the future

## Slide 13: DoE Sea Level Rise Impact on Energy Infrastructure (2014)
National Climate Assessment 2014
But this is just Sea Level
Rise. What about Total
Water Levels?

## Slide 14: Down-scaling Climate Change Impacts

## Slide 15: Digital Elevation Model
Land Elevation is mostly below 4 ft MSL

## Slide 16: What about the Future?
https://tidesandcurrents.noaa.gov/waterlevels.html?id=8534720
We can look to what happen in the past as a proxy for future flooding

## Slide 17: Processing
Start with hourly water levels from Atlantic City
  Use 20 years of observations to Identify high tide peaks and elevations in data set
  1997 – 2017
  De-trend data to remove sea level rise: Left only with high tide elev.
Sandy

## Slide 18: Processing
Develop probability distribution of high tide amplitudes relative to Mean Sea Level
  Analyze data for exceedance probability of High Tides relative to Mean Sea Level
  Provides % time that High Tides were at or above specific elevations
  Assume same distribution will occur with sea level rise
Chart: High Tide Elevation Above MSL at Atlantic City (1997 - 2017)
| -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
 | 1 | 0.99972 | 0.99714 | 0.9848 | 0.94841 | 0.84334 | 0.64708 | 0.41226 | 0.20853 | 0.083176 | 0.023705 | 0.0065537 | 0.0015338 | 0.00020916 | 6.972e-05 | 6.972e-05 | 0

## Slide 19
Chart: High Tide Elevation Above MSL at Atlantic City (1997 - 2017)
| -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
 | 1 | 0.99972 | 0.99714 | 0.9848 | 0.94841 | 0.84334 | 0.64708 | 0.41226 | 0.20853 | 0.083176 | 0.023705 | 0.0065537 | 0.0015338 | 0.00020916 | 6.972e-05 | 6.972e-05 | 0
 | 0 | 1
 | 0 | 1

## Slide 20: Convert to # of High Tides per year
Easier to think in terms of how many high tides per year exceed a specific elevation
  Assume the high tides will continue to follow the 20-year distribution of high tides
  Two high tides per day
  730 total high tides per year
Chart: Annual High Tide Elevations at Atlantic City
| -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
 | 730 | 729.7964 | 727.9133 | 718.9047 | 692.337 | 615.6369 | 472.3649 | 300.9475 | 152.2297 | 60.7188 | 17.3046 | 4.7842 | 1.1197 | 0.15269 | 0.050896 | 0.050896 | 0

## Slide 21: Local Sea Level Rise Projections (relative to year 2000 water level)
Kopp et al., (2016) Assessing New Jersey's Exposure to Sea-Level Rise and Coastal Storms:
Report of the New Jersey Climate Adaptation Alliance Science and Technical Advisory Panel

## Slide 22: Future Sea Level Rise Projections 2030 - 2100
Chart: Annual High Tide Elevations at Atlantic City
| -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
 | 730 | 729.7964 | 727.9133 | 718.9047 | 692.337 | 615.6369 | 472.3649 | 300.9475 | 152.2297 | 60.7188 | 17.3046 | 4.7842 | 1.1197 | 0.15269 | 0.050896 | 0.050896 | 0
0.5 ft SLR | 730 | 730 | 730 | 729.5419 | 725.4194 | 711.3721 | 668.3651 | 567.1331 | 402.1795 | 236.1061 | 109.528 | 37.8666 | 9.8229 | 2.6466 | 0.55985 | 0.10179 | 0.050896 | 0
1.0 ft SLR | 730 | 730 | 730 | 730 | 729.7964 | 726.6409 | 715.5456 | 682.3105 | 592.581 | 437.8575 | 269.0867 | 129.1229 | 47.3332 | 13.182 | 3.5627 | 0.66165 | 0.15269 | 0.050896 | 0.050896
1.64 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 729.5419 | 725.4194 | 711.3721 | 668.3651 | 567.1331 | 402.1795 | 236.1061 | 109.528 | 37.8666 | 9.8229 | 2.6466 | 0.55985 | 0.10179 | 0.050896
3.28 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 729.7964 | 726.6409 | 715.5456 | 682.3105 | 592.581 | 437.8575 | 269.0867 | 129.1229 | 47.3332 | 13.182 | 3.5627 | 0.66165 | 0.15269 | 0.050896 | 0.050896
4.92 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 729.7964 | 727.9133 | 718.9047 | 692.337 | 615.6369 | 472.3649 | 300.9475 | 152.2297 | 60.7188 | 17.3046 | 4.7842 | 1.1197 | 0.15269 | 0.050896 | 0.050896 | 0 | 0
6.56 ft SLR | 1

## Slide 23: Future Flood Events @ Roosevelt Blvd. 2030 - 2100
Chart: Annual High Tide Elevations at Atlantic City
| -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
 | 730 | 729.7964 | 727.9133 | 718.9047 | 692.337 | 615.6369 | 472.3649 | 300.9475 | 152.2297 | 60.7188 | 17.3046 | 4.7842 | 1.1197 | 0.15269 | 0.050896 | 0.050896 | 0
0.5 ft SLR | 730 | 730 | 730 | 729.5419 | 725.4194 | 711.3721 | 668.3651 | 567.1331 | 402.1795 | 236.1061 | 109.528 | 37.8666 | 9.8229 | 2.6466 | 0.55985 | 0.10179 | 0.050896 | 0
1.0 ft SLR | 730 | 730 | 730 | 730 | 729.7964 | 726.6409 | 715.5456 | 682.3105 | 592.581 | 437.8575 | 269.0867 | 129.1229 | 47.3332 | 13.182 | 3.5627 | 0.66165 | 0.15269 | 0.050896 | 0.050896
1.64 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 729.5419 | 725.4194 | 711.3721 | 668.3651 | 567.1331 | 402.1795 | 236.1061 | 109.528 | 37.8666 | 9.8229 | 2.6466 | 0.55985 | 0.10179 | 0.050896
3.28 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 729.7964 | 726.6409 | 715.5456 | 682.3105 | 592.581 | 437.8575 | 269.0867 | 129.1229 | 47.3332 | 13.182 | 3.5627 | 0.66165 | 0.15269 | 0.050896 | 0.050896
4.92 ft SLR | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 730 | 729.7964 | 727.9133 | 718.9047 | 692.337 | 615.6369 | 472.3649 | 300.9475 | 152.2297 | 60.7188 | 17.3046 | 4.7842 | 1.1197 | 0.15269 | 0.050896 | 0.050896 | 0 | 0
6.56 ft SLR | 1
2100 Med
682

## Slide 24: Our Future?

## Slide 25: Our Future?

## Slide 26: Conclusions
Number of flood events changes significantly with small changes in sea level
Daily flooding is likely if sea level rise accelerates at highest scenario rate
Engineering solutions to mitigate future flooding of critical facilities is feasible but surrounding area will likely be flooded.
Joint probability of increased rainfall and high tide flood events is not well understood at this time
  Increased frequency and intensity of rain events will increase frequency of high tide flood events