## Slide 1: Monmouth County coastal lakes, beaches and stormwater
Dr. Jason E. Adolf
Endowed Associate Professor of Marine Science
Monmouth University

## Slide 2: Environmental drivers of ecosystem change
In coastal ecosystems runoff is an important driver of ecosystem variability
  Rainfall is a proxy for stormwater runoff
https://statesummaries.ncics.org/chapter/nj/

## Slide 3: Coastal Lakes and Beaches are two examples of stormwater-impacted ecosystems
Roosevelt Ave. (Deal Fishing Beach)
Monmouth County Coastal Lakes

## Slide 4
Provisional data collected by CLONet citizen scientists
Dr. Jason E. Adolf
Monmouth University
Thanks to the Jules L. Plangere Foundation for support
Secchi depth (ft.)
Water quality varies between coastal lakes and within individual lakes (over time)
Research question: What causes differences?

## Slide 5
Phytoplankton or HAB abundance (RFU)
Harmful algal bloom (HAB) abundance varies between lakes and within lakes (time)

## Slide 6
Which environmental factors correlate best with HAB abundance across coastal lakes?
Total Nitrogen (TN)
Also tested Total Phosphorus, inorganic N and P, pH, water clarity, temperature
  These are important but N-loading of coastal lakes is the main environmental driver of HABs
Our data suggested ample P is already in the lake sediments where HABs form
Storm water can be a source of N and P to lakes, especially lakes found in urbanized watersheds
HAB abundance (RFU)
Total N (mg L-1)
Each point is the average of 16 measurements of HABs and TN, May 2019 – Feb 2020

## Slide 7: We are now focusing on short-term dynamics between rainfall and HABs in coastal lakes
Karly Nolan and Maria Riley, Monmouth University MEBP students
2020 Summer Research Program

## Slide 8
Let’s talk about microbial pollution and rainfall at surfing beaches
Anecdotal links between FIBs, rainfall and stormwater outfalls
Research questions: How well can rainfall predict FIBs at surfing beaches?

## Slide 9
East Long Branch Rainfall Station
(Not Visible)
Lake Takanassee Rainfall Station
Deal Lake
Rainfall Station
Roosevelt Ave. drainage pipe. Representative of stations 4 and 5.
Neptune Ave. drainage pipe (arrow) opening out to sand, rocks and some brush.
Wesley Lake drainage pipe connected to Wesley Lake.
All sites had stormwater outfalls but were not equivalent
‘Ocean Place’
Long Branch
S. Bath Ave.
Long Branch
Roosevelt Ave.
Deal
Neptune Ave.
Deal
Wesley Lake
Asbury Park

## Slide 10
Collect at beaches (between 7am – 10am)
Sterile 50 mL tube for IDEXX
Bucket / 1L bottle for water quality
Hourly rainfall data from http://njdep.rutgers.edu/rainfall/
East Long Branch, Lake Takanassee, and Deal Lake stations
Tested different cumulative rainfall (6, 12, 24h) as well as time-weighted indices as predictors of Enterococcus sp.
Water temperature
Salinity
Dissolved oxygen
Turbidity
pH
Chl a
24h incubation to determine Enterococcus abundance
-US EPA approved method
-Official ATSM Method (#D6503-99)

## Slide 11
Wesley Lk. outfall
Neptune Ave. (Deal)
Roosevelt Ave. (Deal)
S. Bath
Ave. (Long Branch)
‘Ocean Place’ (Long Branch)
Enterococcus sp. (CFU per 100 mL)
Fecal indicator bacteria (Enterococcus) varies beach to beach and within beaches
We used 104 cfu / 100 mL as a threshold value for Enterococcus
125 observations
May 2019 – March 2020
F = 5.4
P < 0.001
a
b
a
a
a, b

## Slide 12
Probability of exceeding safety standard for Enterrococcus
Cumulative rainfall (6h)
‘Ocean Place’
Long Branch
S. Bath Ave.
Long Branch
Roosevelt Ave.
Deal
Neptune Ave.
Deal
Conclusions so far:
Rainfall is a good predictor of Enterococcus
However, even at low / no rainfall sometimes sites were positive
Differences among sites were obvious
These sorts of models can lead to real-time ‘nowcasting’ of microbial pollution based on publicly available rainfall data
P = 0.04
n.s.
P = 0.01
n.s.
Logistic regression models predicted high FIB at 2 of the 4 sites tested

## Slide 13: Conclusion / Synthesis
Coastal ecosystems are complex, but rainfall (e.g. stormwater runoff) appears to explain some of the variability observed in
  Coastal Lake water quality and HABs
  Microbial pollution at surfing beaches
  More to do on both!!
Understanding mechanisms leads to better management
  Predicting effects and measuring efficacy of actions taken
    How well can we quantify (stats!!) the effect of one driver amongst so many?
Good stormwater management will very likely help coastal lakes and beach water quality
  Imagine how many other systems would likewise benefit from good stormwater management!
Watershed characteristics
Stormwater management
ECOSYSTEM EFFECTS

## Slide 14
Questions?
  Jason Adolf, PhD
  Monmouth University
  Biology Department & Urban Coast Institute
  jadolf@monmouth.edu
  732-263-5687
  E274
Thank you for your attention
monmouth_phab_lab
https://jadolf.wixsite.com/phytoplankton
Erin Conlon, Skyler Post, Ariel Zavala, Maria Riley, Karly Nolan, Kelly Hanna, Tori Lohnes, Kaitlyn Saldutti, Sydney Lucas, Jack Campanella, Dr. J. Weisburg
Richard Lee, John Gossart, Jamian Laviola
Robert Schuster, Bill Heddendorf, Eric Ernst, Sherri Shifrin
Acknowledgements
2018
2019
2020