## Slide 1
Scotch Bonnet Island
Marsh Elevation Enhancement: Beneficially Using Dredged Sediments to Stabilize Drowning Marshes
Lenore P. Tedesco, The Wetlands Institute
Monica Chasten, Jeff McAleer - USACE – Philadelphia District
Julie Blum, Amanda Lyons, Lisa Ferguson, Samantha Collins, Brian Williamson - The Wetlands Institute
Ginger Kopkash, Jason Hearon - NJDEP Fish and Wildlife
Brian Harris – USACE – ERDC
Keith VanDerSys and Sean Burkholder – University of Pennsylvania

## Slide 2: Sunny Day Flooding
6/2/2023 2.86’NAVD88
Image Courtesy Ted Kingston
10/30/2023 3.89’NAVD88
Photo: Devin Griffiths

## Slide 3
1956
Fresh Placement and Early Fill
Broad marsh plain with a few isolated pools
Relatively narrow tidal channels
Cape May Wetlands Wildlife Management Area

## Slide 4
1963
Blocked Tidal Channel with Narrow Connection
Road Addition –Salt Marsh Trail
Road Along Scotch Bonnet Creek
Blocked Tidal Channel
TWI Future Site
Stone Harbor Manor/Marina Development

## Slide 5: 1970
Future TWI
Tidal Creek Dead End
Tidal Creek Breach
Creek Expansion/
Disruption from Road
Marsh Conversion
Marsh Pools
Marsh Pools

## Slide 6: 5/2009
Significant Pool Expansion/New Pool Development and Marsh Loss
Low Tide Image So Waterways Show as Mudflats
Tidal Creek Widening and Expansion
Pool Expansion
Pool Expansion
Tidal Creek Widening and Expansion

## Slide 7: Current Marsh Platform Conditions
Tidal Creek Widening and Expansion
Breached Pools
May 2021
New Pools/Pool Expansion
Expanding Creek Network
Channel 70’ Wider since 1970
New Pools/Pool Expansion

## Slide 8: Modelling Future Marsh Trajectory: Sea Level Rise Framework
Utilizing SLR Predictions from Rutgers University
  Values are above the year 2000 (1991-2009 average) baseline
  2000 – 2022 (2001-2019 average) Observed 4” (0.3’)
Planning based on <17% Chance
Focused on 2030 and 2050 Time Horizons
feet
feet
 |  | 2030 | 2050 | 2070 |  | 
 |  |  |  | Emissions |  | 
 | Chance SLR Exceeds |  |  | Low | Mod. | High
Low End | >95% Chance | 0.3 | 0.7 | 0.9 | 1.0 | 1.1
Likely Range | >83% Chance | 0.5 | 0.9 | 1.3 | 1.4 | 1.5
 | ~50% Chance | 0.8 | 1.4 | 1.9 | 2.2 | 2.4
 | <17% Chance | 1.1 | 2.1 | 2.7 | 3.1 | 3.5
High End | <5% Chance | 1.3 | 2.6 | 3.2 | 3.8 | 4.4

## Slide 9: Evolution of Habitat Elevation Ranges
Habitat maintenance over time requires increasing elevations
Presumes salt marsh habitat is primarily guided by elevation related to sea level
TWI elevations determined via direct elevation measurements and USACE 2018 DEM via LIDAR
Future habitat elevation ranges are via SLAMM (Sea Level Affecting Marsh Model) to account for sea level rise, accretion, and subsidence via published resources and measured values

## Slide 10
Scotch Bonnet Island
Southern SMIIL
2020 Existing Conditions

## Slide 11
Scotch Bonnet Island
Southern SMIIL
2030 Projected Conditions

## Slide 12
Scotch Bonnet Island
Southern SMIIL
2050 Projected Conditions

## Slide 13: Scotch Bonnet Island Marsh Elevation Enhancement Project
Project Goals
  Stabilize Failing Marsh Platform
    Increase Marsh Elevation to Stable Low Marsh Elevation Ranges
    Slow Marsh Dissection
  Reverse Marsh Acreage Loss
    1941 to 2019 - Lost 34% of Marsh Area (30 acres)
    Projections to 2050 – Lose Additional 33% (20 acres)
2050 Projected Marsh

## Slide 14: Scotch Bonnet Island Marsh Elevation Enhancement Project
Ecological Targets
  Increase Marsh Platform Resilience by Raising Marsh Elevation into 2030 Low Marsh Elevation Range
    Currently at the Lower Limit of Low Marsh (2.3’NAVD88) near Mudflat Boundary (<2.3’ NAVD88)
    Target 2030 Low Marsh Elevations (2.8’ – 3.5’ NAVD88)
    Maximize Area above 1.8’ NAVD88 – limit of Spartina colonization
  Increase Low Marsh Acreage by Up to 12 acres
  Slow and Reverse Tidal Channel Widening and Expansion

## Slide 15: Scotch Bonnet Island Marsh Elevation Enhancement Project
Placement Method
  Hydraulic cutterhead dredge pumping 25,000 cy of mixed fine sand and mud to site
  Pipeline from dredge site to placement site
  Nozzle outlet pumping onto marsh surface
  Partial coir log containment to direct flows
Timing and Timeline
  Late September - October 2024
USACE Philadelphia District NJIWW Maintenance Dredging
  Critical shoal

## Slide 16: Scotch Bonnet Island Marsh Elevation Enhancement Project
TWI conducting pre- and post-construction monitoring for:
  Elevation enhancement and evolution – multispectral UAV (UPenn)
  Water chemistry impact and evolution
  Pool aquatic habitat surveys
  Vegetation impact and response
  Coastal bird site usage and response to restoration
  Diamondback terrapin site usage and response to restoration
Additional USACE ERDC/USNA Research
  Hydrodynamics of creeks and tidal channels
  Geotechnical response of platform to placement and compaction

## Slide 17: Education and Outreach
Education and outreach will be an important component of the project given the proximity to TWI
Site signage for the trail system
Educational materials for onsite programming and public education
  16,000 school children annually
  18,000 visitors annually
Funding provided by NJ Coastal Wetland Restoration Partnership
2023 Multispectral UAV Imagery
The
Wetlands Institute

## Slide 18: Building Resilience for Cape May Wetland Wildlife Management Area and The Wetlands Institute
Notes: Stressing ecosystems, nuisance street flooding, eroding beaches
Drowning marshes
Drive -2x/day – I SEE CHANGE
Didn’t happen in 1980, 1990, 2000 – happening now!
Doesn’t matter if think human activities contributing – or causing Climate Change
Ice sheets melt, more water, warm water, ocean circulation – more water on land