## Slide 1
Credit: Robin Lubbock/WBUR (www.wbur.org)
Optimized Desing Parameters of Hybrid Vegetation-Seawall Coastal Systems to Enhance Robustness and Flood Serviceability
Reza Marsooli, PhD., Assistant Professor (Stevens Inst. of Tech.)
Erfan Amini, Graduate Research Assistant (Stevens Inst. of Tech.)
Bilal Ayyub, PhD., Professor (University of Maryland)
Marsooli Research Lab
Stevens Institute of Technology
Dept. of Civil, Envir., and Ocean Eng., Hoboken, NJ
rmarsool@stevens.edu | www.marsooli.com
2024 NJ Coastal and Climate Resilience Conference, March 13

## Slide 2: Motivations
Growing coastal flood hazards, and potential environmental impacts of gray (hard, engineering) solutions
Limited capacity of green (soft, natural, nature-based) solutions to mitigate hazards associated with extreme events
Ability of hybrid solutions to benefit from flood reduction benefits of both green and gray solutions and co-benefits of green solutions
Less established design methods for green and hybrid solutions compared to gray solutions (such as seawall)
Long Port, NJ, Jan 2024
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 3: Project Goal and Objectives
Objectives:
Adopt and define practical metrics to quantify the robustness and flood serviceability of the system.
Assess the impact of environmental conditions and vegetation characteristics on the performance of the system.
Find the optimized vegetation characteristics to design effective and efficient hybrid seawall-vegetation systems.
Overtopping
Wave runup
Vegetation
Effect of vegetation?
Goal: to advance understanding of the flood reduction benefits of hybrid seawall-vegetation systems and to develop resilient-based design approaches for such systems.

## Slide 4: Case Study: 17th St. Longport, NJ –profile line# 126
c: December 20, 2017
Atlantic
ocean
Atlantic
city
Ocean
city
- The beach profile is from the New Jersey Beach Profile Network (measurements from the Stockton University Coastal Research Center & NJ Department of Environmental Protection)

## Slide 5
Methods

## Slide 6: Framework
Performance Metrics

## Slide 7
The XBeach-nonhydrostatic model is utilized for modeling wave runup and overtopping of seawall-vegetation systems.
Model validation against experimental datasets
Dataset – Computational Tool

## Slide 8: Dataset – Numerical Experiments Scenarios
Beach Slope Scenarios
5th, 50th, and 95th percentile of measured beach slopes are selected for numerical simulations.
Storm Tide & Wave Scenarios
Three storm tide scenarios.
A synthetic storm dataset (Marsooli et al. 2021) was used to select 50 wave scenarios.
Vegetation Scenarios
Based on the characteristics of spartina alterniflora, five scenarios of vegetation is defined, in which each characteristic was changed by doubled.

## Slide 9
Decision variables are vegetation area (Av), vegetation density (Nv), seawall height (Hsw)
Dataset – Decision Variables and Sampling Space
The Full Factorial Experiment Design method is adopted, by dividing the feasible range for each variable into four equal levels.
The Latin Hypercube Sampling is used to sample scenarios for each of the four levels
3D Sampling Space

## Slide 10
The system can maintain its functionality as long as the overtopping is not occurred.
The robustness of a seawall against a storm event can be quantified by normalized available dry height during the storm.
Dataset – Performance Metric (Robustness)
BFE

## Slide 11
Dataset – Performance Metric (Robustness)

## Slide 12
When the flood level behind the seawall exceeds a threshold (e.g., BFE), the system is no longer capable of providing its intended flood protection, i.e., not serviceable.
Dataset – Performance Metric (Serviceability)
BFE
BFE
BFE
BFE
BFE
BFE

## Slide 13
Objectives and constraints: maximize robustness, minimize costs, and ensuring economically efficient and reliable designs (considering penalties for solutions with serviceability < 50%).
Cost analysis is based on the costs of the hybrid vegetation-seawall system using a methodology outlined in (Greenway et al., 2012) and data from 16 projects in Coastal New England, detailed in (CCRM, 2014).
Optimization – Objectives and Constraints
Total Cost - seawall
Total Cost - vegetation
Total Cost - hybrid

## Slide 14
Train a Gene Expression Programming (GEP) tool for symbolic regression to predict model responses as a non-linear polynomial for untested inputs.
Non-dominated Sorting Genetic Algorithm II (NSGA-II) for multi-objective optimization.
Optimization – Algorithms
Dataset
GEP
NSGA-II
Optimized Design

## Slide 15
Results

## Slide 16: Effects of Beach Slope and Storm Tide
System’s robustness and serviceability are highly sensitive to storm tide across all cases, much more than the beach slope.

## Slide 17
Increasing the stem diameters (Solution II), or enhancing vegetation density (Solution IV), increases the probability of achieving larger robustness and serviceability.
Sol. I: Control scenario
Sol. II: Larger stem diameter
Sol. III: Taller stem height
Sol. IV: Higher density
Sol. V: Larger area
Effects of Vegetation Characteristics

## Slide 18: Optimized Combination of Features (Green/Grey)
The effect of the seawall is more pronounced on the overtopping and robustness of the system.
Increasing the vegetation height can boost the flood serviceability and limit the runup.
Vegetation characteristic
Seawall height

## Slide 19: Optimized Combination of Features (Green/Grey)
The algorithm finds the best solution (design parameters) to maximize the robustness while limiting the total cost.
Final design solutions are different per wave scenario, resulting in an optimized range for each variable.
Possible optimized design:
Hsw = 1 m
Av = 32 sm
Nv = 90 #/sm
There might be an optimum point for design where the maximum performance and minimum cost happens.

## Slide 20
Conclusion:
A multi-objective optimization algorithm integrated with proper system performance metrics can provide a powerful approach to designing effective and efficient hybrid systems for flood adaptation.
Suggestions for the future work:
Including beach erosion in the performance assessment using morphodynamic models.
Assess the effect of vegetation damage during extreme event on the system robustness and flood serviceability.

## Slide 21: Thank you!
Acknowledgement
This project is funded, in part, by the US Coastal Research Program (USCRP) as administered by the US Army Corps of Engineers® (USACE), Department of Defense. The content of the information provided in this publication does not necessarily reflect the position or the policy of the government, and no official endorsement should be inferred. The authors acknowledge the USACE and USCRP's support of their effort to strengthen coastal academic programs and address coastal community needs in the United States.
Contract No. W912HZ22C0010