## Slide 1: Programmatic approach to assessing salt marsh in Delaware and New Jersey for utilizing low-cost low-disturbance methods for enhancing resilience Brian Marsh, USFWS Delaware Bay Coastal Program Kaity Ripple, USFWS Delaware Bay Coastal Program Jim Feaga, Ducks Unlimited, Inc.
Cedar Creek Unit, Milford Neck WA, DE

## Slide 2
What we are doing
Assessing salt marsh sites to:
  find sites suitable for a suite of restoration measures
  gather data useful for design
  gather baseline data

## Slide 3
Murderkill
Dix
Prime Hook Unit IV
Nantuxent
Buckaloo
Port Mahon
Dennis Creek
Cedar Creek
Mispillion
Lighthouse Center
AT&T Tract
Garrison
Where we are working
ASSESSMENT SITES
2023-2024
AREAS OF INTEREST
2022 and onward
Delaware Watershed Conservation Fund - 2022
2023 first field season
2024 second field season

## Slide 4
What do we mean by programmatic approach?
  team approach to developing similar projects across a landscape scale
  economy of scale
  efficient data collection
  standardized protocols
  informed perspective
  sustained partnerships
  learning network
  project pipeline
identify sites
assessment
low-tech design
permitting & funding
installation
monitoring
adaptively manage
completed projects
other restoration methods?

## Slide 5
channels
reference creeks
groundwater
surface water
HYDROLOGY
water levels
local tidal datums
inundation frequency
saturation rate
groundwater level
ditch networks
tidal lag and restriction
trapped hydrology
Onset HOBO
Hyfi
What we are assessing

## Slide 6
RTK
LiDAR
ELEVATION
RTK and LiDAR data
predicting inundation patterns
revealing elevation deficits
determining if elevation capital is present
0.5 ft
1.1 ft
-1.5 ft
ditch
microberm
inundated
marsh
What we are assessing

## Slide 7
horizontal vegetation
obstruction
vegetation height
% cover and composition
bio-benchmarks
VEGETATION
composition, density, condition
indicator of hydrology
indicator of trajectory
What we are assessing
predetermined point grids

## Slide 8
BEARING CAPACITY
centimeters of penetration depth
indicator of peat and root condition with greater penetration depths suggestive of peat breaking down and poor root vigor
capabilities of substrate to support restoration features
What we are assessing

## Slide 9
AVIAN COMMUNITY
tidal marsh bird point counts
habitat indicator
important conservation species
What we are assessing

## Slide 10
NEKTON COMMUNITY
community coming off the marsh on ebb tides
habitat indicator
important trophic species
What we are assessing

## Slide 11
ONLINE GIS TOOL
Used For
planning surveys
evaluating data and designs collaboratively
final designs exported to design plans/specs for permitting and construction
Incorporates
ownership
marsh features
remote sensing data
field data
georeferenced site pictures
How the data is being gathered

## Slide 12
mean sea level
healthy marsh
degrading marsh
lost marsh
ELEVATION
TIME
What are low-cost low-disturbance restoration methods
push marsh towards self-healing
potential stopgap measures
low-cost
low-disturbance
rapid implementation
allow for in-field decisions
rapid results
integrable with other methods
scalable, replicable
low risk
easy adaptively managed
  “low-tech” approaches enhance resilience and habitat by improving salt marsh vegetation via minor changes to hydrology, elevation, and other parameters

## Slide 13
features placed along eroding edges or across expanding mudflats within salt marsh to:
coir logs
Natural Lands’ Garrison Tract
Dix WMA
haybales
Dennis Creek WMA
brush fences
MarshGuards
Technique: Biodegradable and temporary structures
  reduce fetch
  attenuate wave energy
  promote sediment accretion
  allow revegetation

## Slide 14
Bayshore mudflat sites, Cumberland and Cape May Counties, NJ
Nantuxent
Dennis
Dix
Garrison
Dennis Creek WMA
Dix WMA
Nantuxent WMA
Natural Lands’ Garrison Tract
remnants of impounded marsh
intertidal
unstable edges
mobilized sediment and loss
vegetation struggling to reestablish
Technique: Biodegradable and temporary structures

## Slide 15: Ditches initially cause oxidation and loss of elevation -> higher water table and microberms lead to a hypersaturated marsh surface -> vegetation die-off, accretion lag, and pool formation -> pool expansion and merging of neighboring pools.
Technique: Runnels
Water trapped on surface
Low berm allowing water to come in on flood tide but preventing water from leaving during ebb tide
functional intertidal channel
Smith et al. (2021)

## Slide 16
Reconnecting saturated marsh to functional tidal channels
Reduces platform saturation or inundation
Reintroduces tidal cycle
Increases vegetation vigor
Allows revegetation
Technique: Runnels
Wenley Ferguson 2020
Rum Pointe, MD
Great Marsh, Parker River NWR

## Slide 17
Great Marsh, Parker River NWR
Technique: Runnels
AT&T Tract, EBF NWR, Manahawkin 2022

## Slide 18
Murderkill
Murderkill (Hall Tract), Milford Neck Wildlife Area, DE
saturated areas but still with elevation capital
1936
Technique: Runnels

## Slide 19
Strategic full or partial filling of sections of ditch to promote a more natural network of tidesheds and channels.
Decreases channel overlap
Increases channel efficiency
Technique: Ditch remediation
Natural tideshed
Grid ditching

## Slide 20
Burdick et al. (2020): Mitigating the Legacy Effects of Ditching in a New England Salt Marsh
Ditch remediation adds vegetation and elevation
Technique: Ditch remediation

## Slide 21
AT&T Tract, Edwin B. Forsythe NWR, Ocean County, NJ
AT&T Tract
long mosquito ditches draining towards multiple directions creating low energy ineffective channels
Technique: Ditch remediation

## Slide 22
Technique: Ditch maintenance
Removing naturally formed ditch plugs to reopen select ditches
Restore tidal flow
Reduce impounded water
Reduce saturation of neighboring marsh
Natural Ditch Plugs
DU - Parker River NWR

## Slide 23
Mispillion
Mispillion Marine Reserve, DE
ditch ponding
Technique: Ditch maintenance

## Slide 24
  Small-scale use of material to increase marsh platform elevation heterogeneity and substrate suitability to enhance marsh vegetation
Increase positive relief to restore flow off the marsh
Increase productivity
Increase habitat heterogeneity
Technique: Substrate and elevation enhancement with organic material
????
Good Luck Point, EBF NWR

## Slide 25
Cedar Creek
Cedar Creek Tract, Milford Neck Wildlife Area, DE
vegetation die-off
low production
Technique: Substrate and elevation enhancement with organic material

## Slide 26
New Jersey Fish and Wildlife
Delaware Division of Fish and Wildlife
Partnership for the Delaware Estuary
Conserve Wildlife Foundation of New Jersey
National Fish and Wildlife Foundation
Hyfi
Enostat
Drexel University
National Wildlife Refuge System
The Nature Conservancy
Delaware Center for the Inland Bays
Lighthouse Center for Natural Resources Education
NJDEP Division of Science and Research
Coastal Technologies Corp
Delaware Mosquito Control Section
New Jersey Mosquito Control Commission
…and future partners
This is a partnership-based effort!

## Slide 27
Kaity Ripple: kaitlyn_ripple@fws.gov
Brian Marsh: brian_marsh@fws.gov
Jim Feaga: jfeaga@ducks.org
Kaity Ripple/USFWS